## Slide 1
TAIEX
Temporary expert assignment
(within the framework of transfer of Czech transitional expertise)
- CONSTRUCTION PRODUCTS -
Technical regulation and Standards, Authorization, Notification, Quality infrastructure
Václava Holušová
Podgorica, September 25-26, 2018

## Slide 2: Construction products on the common European market
Special position of construction products (CP):
New Legislative Framework, established by Regulations 764/2008 and 765/2008 of the European Parliament, plus Decision 768/2008 of the EP, is applicable on CP only partially. That´s why the official guiding document for implementation of EU product rules (so-called Blue Guide) does not apply on CP.
Unlike other types of products, CP cannot be used as such; they need to be incorporated in the building first. Different nature of CP leads to a different approach to testing (different modules than described in Dec. 768/2008).
Two cathegories of CP – harmonized and non-harmonized
Mutual recognition
TRIS database

## Slide 3: Regulation 305/2011 on Construction Products (CPR) – part 1
What is the basic statutory instrument for construction products in the EU?
Construction Products Regulation (the CPR) is a legislative act adopted by European Commission in April 2011 that:
Applies for construction products covered with harmonized European standards
Lays down harmonized conditions for the marketing of construction products
Replaced a previous European legislative, Construction Products Directive (CPD)
Describes stricter and more transparent procedures for introducing these construction products with CE marking to the common EU market
Came into full force since July 1st, 2013
Is obligatory for all countries belonging to the European Economic Area (EU members plus Iceland, Liechtenstein and Norway)

## Slide 4: Regulation 305/2011 on Construction Products (CPR) – part 2
What ´s the aim of CPR? (according to the official website of European Commission)
Construction Products Regulation (the CPR) is to ensure reliable information on construction products in relation to their performances. This is achieved by providing a “common technical language", offering uniform assessment methods of the performance of construction products. These methods have been compiled in harmonised European standards (hEN) and European Assessment Documents (EAD).
This common technical language is to be applied by:
the manufacturers when declaring the performance of their products, but also by
the authorities of Member States when specifying requirements for them, and by
their users (architects, engineers, constructors…) when choosing the products most suitable for their intended use in construction works.

## Slide 5: Regulation 305/2011 on Construction Products (CPR) – part 3
Official report on the implementation of the CPR according to Art. 63(1) was published in April, 2016 by the Commission and submitted to the European Parliament and Council. No objections were raised yet.

## Slide 6: Harmonized standards under the CPR part 1
A harmonised standard is a standard adopted by CEN on the basis of a request issued by the Commission (formerly called „mandate“, now it is known as „standardization request“). Only part of the standard becomes harmonised under the CPR.
Standards are voluntary but a special annex to the standard known as Annex ZA includes the details which serves as a tool for assessment of the performance of construction products under the CPR. Informative Annex ZA becomes mandatory for the use of the standard under the CPR.
Annex ZA:
  identifies the essential characteristics related to the BWR for the construction products covered by the standard
  defines the system of AVCP in order for the manufacturer to:
    draw up a DoP
    affix the CE marking
  provides the AVCP tasks for the manufacturer and the notified body (if any)

## Slide 7: Harmonized standards under the CPR part 2
List of harmonized European Standards is published in the Official Journal of the European Union (OJEU) regularly, ca. 2 times a year. European Assessment Documents are published ca. 3 times a year. Only standards on which consensus was reached throughout the EU can be published in OJEU.
A new version of a hEN cannot automatically be used as a hEN under CPR which is sometimes confusing. Actually CEN (European Committee for Standardisation) has prepared ca. 100 hENs which cannot be published in OJEU because of conflicting parts (they either don´t fulfill the mandates completely, or go above them, or some MS raised complaints).
Joint Initiative on Standardisation (JIS) started in June, 2016. This initiative should bring all stakeholders together to improve the implementation of the CPR in standardisation. Construction products were chosen as a pilot project for improving the co-operation between DG Growth and CEN.
Many hENs have been adopted before the CPR came into force, so they were not created with respect to it. It´s important to keep on mind that the CPR always prevails over any part of a hEN which can be in a contradiction.

## Slide 8: Declaration of Performance (DoP)
The Declaration of Performance (DoP) is the key concept in the Construction Products Regulation (CPR).
The DoP gives the manufacturer the opportunity to deliver the information about the essential characteristics of his product he wants to deliver to the market.
The manufacturer, by drawing up his DoP, assumes the responsibility for the conformity of the construction product with the declared performance.
On the basis of the information contained in the DoP, the user will decide to buy, amongst all the products available on the market, the one which is fit for the use he intends to give to such product and he assumes the full responsibility of such decision.
The minimum amount of information that the manufacturer is obliged to provide is set up in Art. 6 of the CPR.

## Slide 9: CE marking
The CE marking follows the DoP and means that the manufacturer has strictly followed all the applicable procedures for drawing up his DoP and, consequently, the DoP is accurate and reliable.
„CE marking step-by-step“ – an information guide created by the Comission in all languages of Member States, to help spreading information amongst the manufacturers.
CPR is an open document. Some articles (f.e. 5, 36, 37) still need to be interpreted uniformly. Working groups on common interpretations have been established. It´s not easy to create a common approach amongst so many countries.
Documents – „guides“ which were adopted for the interpretation of the previous legislation „CPD“ are no longer officially valid for the CPR. Still they can serve as a source of valuable information.

## Slide 10: CE marking
The industry calls for a European harmonised electronic format to enhance the delivery of information to the market. This common electronic format is a precondition for interaction and compatibility between IT tools, be it software or databanks, from different developers.
Construction Products Europe Aisbl. (association of European construction products manufacturers, from SMEs to multinational companies.) came with an initiative called „Smart CE-marking“– they encourage the Commission to launch the development of a European harmonised electronic format, both human and machine readable, to boost the usability of the regulatory information and the compatibility with existing or future digital systems. In particular declaration of performance of construction products.
European harmonised electronic format will facilitate private or national initiatives to develop websites, apps, databanks, software and any IT tools to address the needs of regulators, markets and/or customers.

## Slide 11: Delegated acts
The Construction Products Regulation (CPR) allows the Commission to adopt legal acts to implement or to complement the CPR, either in the form of implementing or delegated acts mentioned in Articles 26(3) and 60 of the CPR respectively.

## Slide 12: Construction products in the Czech Republic
Construction products in the Czech Republic:
System of state guaranteed testing
Distribution of responsibilities in harmonized and non-harmonized sphere
Lessons learned from the process of implementation of the CPR

## Slide 13: ACT No 22/1997 COLL., ON TECHNICAL REQUIREMENTS FOR PRODUCTS – part 1
ACT No 22/1997 COLL., ON TECHNICAL REQUIREMENTS FOR PRODUCTS
Article 1 - Scope
(1) The Act lays down
a) the method of establishing technical requirements relating to products which are likely to pose a higher degree of danger to public health and/or safety, property or environment or another public interest (hereinafter referred to as “justified concern“),
b) the rights and obligations of the persons who place on the market or distribute or put into service products which are likely to pose a higher degree of danger to the justified concern; this is without prejudice to the provisions of special laws relating to the operation of products1),
c) the rights and obligations of persons designated to carry out activities under this Act relating to the drafting and application of Czech standards or to State testing,
d) the method of ensuring information obligations relating to development of technical regulations and standards resulting from international agreements and requirements of the law of the European Communities.

## Slide 14: ACT No 22/1997 COLL., ON TECHNICAL REQUIREMENTS FOR PRODUCTS – part 2
(2) Following the directly applicable regulation of the European Communities this Act furthermore regulates the accreditation of conformity assessment bodies (hereinafter referred to as “accreditation”).
(3) Following the directly applicable regulation of the European Union on construction products this Act furthermore lays down the exercise of state administration in connection with placing and making available on the market of construction products defined by the directly applicable regulation on construction products (hereinafter referred to as “construction products bearing the CE marking”) including the market surveillance on the compliance with the obligations laid down by directly applicable regulation on construction products and the sanctions for their infringement.

## Slide 15: ACT No 90/2016 COLL., ON ASSESSMENT OF CONFORMITY OF SPECIFIED PRODUCTS PLACED ON THE MARKET
(This new act is not available in English yet.)
It implements the EU legislative on a common framework for the marketing of products (Decision 768/2008 of the European Parliament) and lays down the exercise of state administration concerning products which are likely to pose a higher degree of danger to life, public health and/or safety, property or environment or another public interest.
This act sets the rules for notifying and supervising all Czech Notified Bodies, including the NBs under the CPR. So since April 15, 2016 all Czech NBs are treated the same way. Subjects already notified according to the previous legislative (Act No. 22/1997 Coll.) are understood as if they were notified according to this new act.

## Slide 16: Two cathegories of construction products
Two cathegories of construction products falling under a system of state-guaranteed testing:
Harmonized sphere: Construction products covered by European harmonized standards or for which a European Assessment Document has been issued in accordance with regulation (EU) No 305/2011 (CPR)
Non-harmonized sphere: Products that are not covered by harmonized standards or that are not in accordance with the European Technical Assessment can not be CE marked. These products are assessed according to the regulations of the State where they are placed on the market. It is Government Regulation no. 163/2002 Coll. as amended Government Orders No. 312/2005 and 215/2016 Coll. in the Czech Republic in this case.

## Slide 17: Harmonized sphere
Construction product covered by European harmonized standards
Act no. 90/2016 Coll., § 23 - Notified bodies (NBs)
The legal entity can carry out the activities of notified body only if in the proceeding conducted by the Office and started upon the application demonstrates the conformity with the requirements of the notified body laid down in the Article 43 of directly applicable regulation on construction products. The Article 47 of directly applicable regulation on construction products lays down the requirements of the application on the issuing the authorization to carry out the activities of notified body (hereinafter referred as “authorization”).
Act no. 22/1997 Coll., Article 11c - Technical assessment bodies (TABs)
The Ministry may designate a legal entity to carry out activities of technical assessment body on the basis of its application provided that the body meets requirements laid down in directly applicable regulation on construction products.

## Slide 18: Czech Office for Standardization, Metrology and Testing
Testing Department is a part of the Office which is responsible, in particular, for ensuring the state testing to the extent provided by the Act No. 22/1997 Coll., on Technical Requirements for Products and Act No. 90/2016 Coll., on assessment of conformity of specified products placed on the market; and the governmental orders issued to implement these Acts.
    Testing Department has been designated as a national notifying authority (Art. 40 of the CPR), responsible for setting up and carrying out the procedures for the assessment and notification of the so-called third parties in the process of assessment and verification of constancy of performance.
    TD also performs the monitoring of notified bodies, including their compliance with all the demands of Art. 43 of the CPR.
Distribution of responsibilities concerning a process of notification:
The Office is a Notifying Authority for Notified Bodies (NBs)
The Ministry of Industry and Trade is a Designation Authority for Technical Assessment Bodies (TABs)
(This distribution of roles is not common amongst the Member States; usually the roles of Notifying Authority and Designating Authority are performed by one institution.)

## Slide 19: Czech Office for Standardization, Metrology and Testing
    The Office offers an internet service for companies and individuals who need to get an access to the Czech Technical Standards on-line; this service is operated on a commercial basis: http://www.unmz.cz/urad/csn-on-line
    The Office also runs a very sophisticated information database for everyone who is either professionally or privately interested in construction products, placed on the common EU market. Substantial part of the information is available in English language as well.

## Slide 20: Information Portal - Construction Products
I. Construction products with CE marking
For each construction product covered by a European harmonized standard or for which a European Technical Assessment has been issued in accordance with regulation (EU) No 305/2011 (CPR) Declaration of performance shall be draw up and CE marking shall be affixed. Useful tools to meet these obligations are:
Harmonized standards database for CPR (+ actual changes)
Assignment of harmonized standards to groups of products (according to CPR, Annex IV)
Horizontal specifications
European Assessment Documents - EAD (ETAGs used as EADs)
Czech notified bodies and technical assessment bodies (TAB) to CPR
Assessment and Verification of Constancy of Performance:
System 1+, System 1, System 2+, System 3, System 4
Basic work requirements:
No. 1 - Mechanical resistance and stability
No. 2- Safety in fire
No. 3 - Hygiene, health and the environment
No 4 - Safety in use
No. 5 - Protection against noise
No. 6- Energy economy and heat retention
No. 7 - Sustainable use of natural resources
Czech Product Contact Point For Construction
Frequently asked questions

## Slide 21: Information Portal - Construction Products
II. Construction products without CE marking
Products that are not covered by harmonized standards or that are not in accordance with the European Technical Assessment can not be CE marked. In accordance with CPR, these products are assessed according to the regulations of the State where they are placed on the market. It is Government Regulation no. 163/2002 Coll. as amended Government Order No. 312/2005 Coll. in the Czech Republic in this case.
List of specified standards to Government Order No. 163/2002 Coll.
List of Czech authorized bodies with scope of authorization for selected construction products
Product groups according to Annex No. 2 Government Order No. 163/2002 Coll., with assigned equivalent technical guides, conformity assessment procedures, activities of authorized bodies:
Construction products for concrete and reinforced concrete parts of construction works
Construction products for masonry works
Construction products for wood and timber products and timber constructions
Construction products for metal constructions
Protective, thermal and sound insulating materials and products, waterprooofing materials, roof coverings and adhesives
Construction glass products
Construction products for waste water engineering and liquid and gas distribution system
Construction products for opening closures
Special materials, products, structures and equipment
Technical equipment of buildings
Construction products for internal and external wall, ceiling and floor finishes
Construction products for sanitary appliances

## Slide 22: Information Portal - Construction Products
III. Other useful information
Eurocodes
Czech legislation relating to the construction products
Czech legislation relating to construction works
Abbrevitations
Commission Decisions (CPD)
Mandates CEN/CENELEC (CPD)
Mandates EOTA for ETA (CPD)
All harmonized standards (not only CPR) grouped by sectors
Searching in harmonized standards database for all sectors

## Slide 23: Notification and designation
Notification is an act whereby a Member State informs the Commission and the other Member States that a body, which fulfils the relevant requirements, has been designated to carry out conformity assessment according to a directive. Notification of Notified Bodies and their withdrawal are the responsibility of the notifying Member State.
Notification and designation procedures had to be approved by the Commission prior to the notifying. Member states have to describe thei way how they treat the subjects applying for a role of a NB. An important part of this procedure is a declaration whether the notification will be based on accreditation (and which accreditation standards EN ISO/IEC 17000 will be preferred), or not. The Commission strongly prefers the accreditation way. All notification procedures of Member States are collected in NANDO and can be viewed under this link.
NOTE: If a subject wants to be notified as NB and designated as TAB at the same time, it is necessary to submit an organizational scheme which clearly shows how these two roles will be managed separately and independently. It was a case of both Czech TABs, and the Commission was very careful when assessing their organizational schemes.

## Slide 24: Guidelines for the evaluation of TABs part 1
The purpose of this document is to launch the debate on the content of the guidelines necessary to be established for the evaluation of Technical Assessment Bodies (TABs) in accordance with Article 29 of the CPR. After the SCC meeting of 13 – 14 February 2014, Member States will be awarded a period for presenting their additional remarks in writing, so as to allow for the decision-making to take place timely for the practical needs.
According to Article 29(3) of the CPR, Member States are in charge of the monitoring the activities and competence of the TABs they have designated, and of their evaluation in relation to Table 2 of Annex IV. Member States have also been tasked to inform the Commission about these activities of theirs and the results thereof. In accordance with Article 29(4),
“[t]he Commission shall adopt guidelines for carrying out the evaluation of TABs, after consulting the Standing Committee on Construction”.

## Slide 25: Guidelines for the evaluation of TABs part 2
The application activities of the CPR have started on 1 July 2013, with 18 TABs designated and confirmed in NANDO-CPR at that time. By now, this number has grown to 29; out of them, 7 have been designated for a given period of time (some of them elapsing in 2014). This fact prompts to the process at hand, the adoption of the guidelines for the evaluation activities, which would appear an appropriate pre-requisite for the respective Member States when reconsidering these designations.
For those TABs which have been designated for an unlimited period, a general decision would appear opportune to be taken about the frequency of their evaluation: the question is, how many years could be seen as the optimal frequency here. It could also be considered useful to establish a maximum number of years, after which time this evaluation would have to be carried out.

## Slide 26: Guidelines for the evaluation of TABs part 3
The CPR does not contain any provisions of the potential peer review elements in these evaluations: rules on this aspect were proposed by the Commission, after input from notably EOTA, but the co-legislators, in particular the Council, decided not to include them in the final text. This issue links to the benefits accrued / disadvantages caused by the involvement of EOTA and/or TABs themselves in these processes. It could be asserted that peer review elements would bring into the evaluations more hands-on experience on the activities at hand, those to be evaluated, and thus increase the added value of these processes.
As the monitoring of TABs, to be carried out by the respective Member States, also comprises (or is linked to) informing the Commission about these matters, it would appear rational to combine these transmissions to the context at hand. Member States certainly are compiling certain basic data of the functioning of their TABs: notably the number of ETAs requested and issued, the participation into the development of EADs, the average costs of ETAs for manufacturers, the funding scheme of the CPR –based actions of the TAB and the percentage related to the application of the CPR of all activities of the organisation serving as a TAB. These pieces of information would thus form the natural factual base of the evaluation to be carried out.

## Slide 27: Guidelines for the evaluation of TABs part 4
The obvious starting point for the core evaluation would be formed by the answers the designating authorities of Member States have transmitted to the Commission to the “10 questions” from the document distributed in the autumn of 2011 to all Member States as practical advice how to operate the new NANDO-CPR. The first check would again naturally consist of, whether this information had changed in any way. These eventual changes in the pertinent circumstances would then also have to be signalled to the Commission pursuant to Article 29(3) of the CPR. In the same context, it should be considered whether this information (the up-to-date set of these answers) were to be made publicly available; the same goes for the evaluation results more in general.
In case Member States wished to emphasise certain focal areas, to be concentrated upon when carrying out the evaluation at hand, suggestions for such areas would certainly be considered welcome. Of course, also other stakeholders might bring forward their opinions in this respect. Judged by the discussions both before and after the adoption of the CPR, one could assume that the issues of the independence of TABs from undue influence and their respect of good administrative behaviour could well come on top of the list of priorities here.

## Slide 28: NANDO Information System
NANDO (New Approach Notified and Designated Organisations) Information System of the Commission
NANDO is a place where Notifying Authorities insert and maintain files of Notified Bodies and TABs they have designed. NANDO contains records of all NBs established for every directive or regulation, not only construction products. The lists include the identification number of each NB as well as the tasks for which it has been notified, and are subject to regular update. The lists of notified bodies are given for information only and are valid at the date indicated. Information is made available as provided by the designating authorities of the Member States, EFTA countries (EEA members) and other countries with which the EC has concluded Mutual Recognition Agreements (MRAs) and Protocols to the Europe Agreements on Conformity Assessment and Acceptance of Industrial Products (PECAs).
A guidebook to using NANDO can be printed out from this link.

## Slide 29: NANDO 1/3

## Slide 30: NANDO 2/3

## Slide 31: NANDO 3/3

## Slide 32: Czech timing of notification and designation
Helping the „old“ NBs notified under a directive CPD to become „new“ NBs under a regulation CPR
Applications of NBs-to-be could be officially registered only after May 10, 2013 when an amendment of act No 22/1997 Coll. came into effect, designing the Office for Standards, Metrology and Testing as a National Notifying Authority. Due to the short time between May 10 and July 01, 2013, it was necessary to work with our NBs to be sure that their applications will fulfill all the necessary administrative demands at the „D-day“. The Office published a detailed „cookbook“ containing all demands of CPR and ways how to prove a fulfillment. Consultations with „old“ NBs had been taking place for several months because it was rather difficult for them to create an application which could satisfy the Office.
All Czech subjects applying for a role of a third independent party under CPR were notified successfully so that they could start working at the first days of July, 2013.

## Slide 33: Horizontal notification of NBs
Notification for a single characteristic („horizontal specification“) is a concept aimed at the Testing Labs operating under AVCP 3. Certification bodies have to be notified against hENs.
HORIZONTAL SPECIFICATIONS IN THE CPR
Annex V clause 3: Assessment and verification of constancy of performance « Case of essential characteristics where reference to a relevant harmonised technical specification is not required » 1. Reaction to fire 2. Resistance to fire 3. External fire performance 4. Noise absorption 5. Emissions of dangerous substances
There are 39 horizontal specifications in NANDO at the moment, vast majority of them falling under cathegories 1 to 3 (related to fire). Notification in the Czech Rep. is based on accreditation, that means a Testing Lab has to be accredited against these horizontal specifications in the accreditation certificate according to EN ISO/IEC 17025.

## Slide 34: Coordination of NBs 1/2
Activities of the Office towards the NBs of course did not stop in the moment of their notification in NANDO. Actually the Testing Department is in contact with them on various levels, in order to fulfill our role of a Notifying Authority.
Coordination of NBs according to Art. 55 of the CPR:
Member States shall ensure that the bodies notified by them participate in the work of that group, directly or by means of designated representatives, or shall ensure that the representatives of notified bodies are informed thereof.
The Office authorized a Technical and Test Institute for Construction Prague (Authorized Body 204, Notified Body 1020, Technical Assessment Body) to perform coordination activity of authorized bodies / notified bodies / technical assessment bodies in assessing the conformity of construction products. This coordination role is supported financially by the Office on annual basis and a representative of Testing Department contributes to its work.

## Slide 35: Coordination of NBs 2/2
This activity includes, in particular:
establishment of the Coordination Office Committee, which is an advisory body of the Czech Office for Standards, Metrology and Testing and of the Coordination Office;
ensuring the information communication between working groups, Czech Trade Inspection Authority and representatives of the business sector;
ensuring the creation and updating of technical guidelines for conformity assessment under Government Regulation No. 163/2002 Coll., as amended, in working groups of the authorized body;
ensuring the coordination procedure of notified bodies in accordance with the CPR;
ensuring the activity of the Coordination Office as mirror activity to the Advisory Group of Notified Bodies for the CPR (AG NB);
transferring information from European institutions to Czech authorized bodies / notified bodies, organizing the participation of specialists in sector working groups of notified bodies and EOTA working groups;
preparation and distribution of methodological materials.

## Slide 36: Accreditation – part 1
All Czech NBs are accredited by a National Accreditation Body –
Czech Accreditation Institute (Český institut pro akreditaci) which declares to provide unambiguous, objective and independent assessment of competence of the following entities relevant for construction products testing:
Testing Laboratories (EN ISO/IEC 17025:2005)
Calibration Laboratories (EN ISO/IEC 17025:2005)
Inspection Bodies (EN ISO/IEC 17020:2005, EN ISO/IEC 17020:2012)
Certification Bodies for certification of quality management systems, environmental management systems, occupational health and safety management systems, information security management systems, food safety management systems and sustainable forestry management system (EN ISO/IEC 17021:2011)
Certification Bodies for certification of products and processes, including certification of chain of custody of wood, qualification of building contractors (EN ISO/IEC 17065:2013)

## Slide 37: Accreditation – part 2
Czech Accreditation Institute is a member of international organizations (EA, ILAC, IAF) and a signatory of the multilateral agreements of EA (European level), ILAC and IAF (world level) on mutual recognition of results of accreditation.
A cooperation between the Office and is an important tool for maintaining a high level of competence and professionality of Czech NBs.
Two types of accreditation:
Accreditation against standards (without relation to a particular EU directive or regulation)
Accreditation for notification (covers also some demands of a particular EU directive or regulation)
Our Office deals with both types of accredited subjects.

## Slide 38: Product Contact Point for Construction – part 1
Member States are obliged to design the Product Contact Point for Construction (PCPC) according to Article 10 of the CPR.
The PCPC ensures the accessibility of national technical rules relating to construction products in the Czech Republic and provides information on provisions aimed to fulfill basic requirements for construction works applicable for the intended use of construction product. The PCPS advises free of charge, with a 15-day time limit to response.
Contact e-mail: cpr@mpo.cz
In the Czech Republic, the PCPC is operated by the Ministry of Industry and Trade. 50 % of all inquiries came from abroad. Inquiries from EU Member States are prevailing (esp. Poland and Germany).
A list of PCPCs in all Member States is available from the Commission website.

## Slide 39: Product Contact Point for Construction – part 2
The most frequent questions concerning the CPR based obligations are aimed at:
Declaration of performance (DoP)
Language demands
Validity of certificates
Art. 5 - exceptions from DoP
Art. 8(4) and FAQ 23 - additional national demands on products with CE marking
Legality of CE marking a particular product
Obligations to supply additional documents together with DoP
Link to the PCPC:
http://www.mpo.cz/dokument142120.html in English
Link to FAQs:
http://www.mpo.cz/zprava157664.html in English

## Slide 40: Standing Committee on Construction; CIRCABC
Member states shall nominate their representatives to the Standing Committee on Construction (SCC) which is an advisory group according to Art. 64 of the CPR.
Member States shall ensure that the members of the SCC are able to carry out their functions in a manner that avoids conflicts of interest, particularly in respect of the procedures for obtaining the CE marking. Each Member State shall be considered to be one member of the committee. Each member of the committee shall decide on the composition of its delegation and inform the chair. With the chair's permission, the delegations may be accompanied by experts who are not part of the delegation.
Documents issued for the purposes of the SCC are stored in a special file in the CIRCABC - Communication and Information Resource Centre for Administrations, Businesses and Citizens. Members of the SCC are given an access to cathegories and interest groups they ask for (and are approved by the administration).
Link to CIRCABC main page: https://circabc.europa.eu/faces/jsp/extension/wai/navigation/container.jsp

## Slide 41: Barriers to trade
The European Court of Justice: The Commission over the German barriers to trade in construction products
German requirements that construction products must have additional national marks or approvals, despite the fact that they already have a CE-mark and are legally marketed in other Member States, are breaching the European rules of free movement of goods.
This was confirmed by the European Court of Justice on 16/10/2014. Such an outcome represents a significant step forwards for the consolidation of the Internal Market for construction products.
This national system requires construction products that are already CE-marked to undergo additional testing and acquire national approval, before they can be marketed in Germany. The Commission had received numerous complaints from manufacturers and importers of construction products, who have had difficulties to sell their products on the German market.
The judgement of the Court impacts the whole German system of „Bauregellisten“ but also other EU member systems of national demands.
http://ec.europa.eu/growth/tools-databases/newsroom/cf/itemdetail.cfm?item_id=7860&lang=en

## Slide 42: Barriers to trade
Possible solution?
Germany was recommended to apply an Art. 18 of the CPR and raise formal objections against those harmonised standards it considers them not entirely satisfying the requirements set out in the relevant mandate.
Germany raised formal objections against 7 harmonised standards already.
Next steps: first a consultation of the Standing Committee on Construction, then the Standards Committee operating under Standardisation Regulation.
The possible outcomes of formal objections can be as follows:
1) Maintain the reference in OJEU
2) Maintain the reference with restriction
3) Withdraw the reference from OJEU
http://ec.europa.eu/growth/tools-databases/newsroom/cf/itemdetail.cfm?item_id=7860&lang=en

## Slide 43: Non-harmonized sphere
Construction products not covered by harmonized standards or that are not in accordance with the European Technical Assessment:
Act no. 22/1997 Coll., Article 11 - Authorization
For the purpose of this Act authorization shall mean the designation of a legal entity for activities concerning conformity assessment of products including assessment of activities connected with manufacture or reuse of products and specified in technical regulations (hereinafter referred to as „authorized body“). Authorization for activity under this Act shall be granted, with a defined scope by the decision of the Office based on an application which must be supported by evidence of authorization conditions fulfilment laid down in this Act and in the Government Orders. In the case of application on authorization to conformity assessment for products specified in a Government Order the description of procedures and other conformity assessment activities shall be a part of the application. The Office shall ensure an observance of a uniform procedure in the activities of the authorized bodies.
Act no. 22/1997 Coll., Article 11a - Authorized bodies
Authorized bodies shall ensure activities within the scope defined in the decision on authorization.

## Slide 44: Mutual recognition – part 1
Based on Regulation (EC) No 764/2008
Guidance document (not legally binding) from October 13, 2011, issued by the Commission:
The application of the Mutual Recognition Regulation to non-CE–marked construction products
The Regulation applies to administrative decisions addressed to economic operators, on the basis of a technical rule, in respect of any non-harmonised product lawfully marketed in another Member State, where the direct or indirect effect of that decision is the prohibition, modification, additional testing or withdrawal of the product. Any authority intending to take such a decision must follow the procedural requirements in the Regulation.

## Slide 45: Mutual recognition – part 2
The Regulation will apply when all the following conditions are met:
  The (intended) administrative decision must concern a product lawfully marketed in another Member State
  The (intended) administrative decision must concern a product which is not subject to harmonised EU law
  The (intended) administrative decision must be addressed to an economic operator
  The (intended) administrative decision must be based on a technical rule
  The direct or indirect effects of the (intended) administrative decision must be any of the following:
(a) prohibition of the placing on the market of that (type of) product;
(b) modification or additional testing of that (type of) product before it can be placed or kept on the market;
c) withdrawal of that (type of) product from the market.

## Slide 46: Mutual recognition – part 3
The (intended) administrative decision must concern a product lawfully
marketed in another Member State
The principle of mutual recognition applies where a product, irrelevant of its actual
origin (EU or third country import), lawfully marketed in one Member State is
placed on the market in another Member State. Following this principle, a Member
State cannot in principle forbid the sale on its territory of products which are lawfully
marketed in another Member State, even if they were manufactured according to
different technical rules. Both actual and possible denials of mutual recognition are
governed by the Regulation. Hence, any Member State intending to ban access to its market should follow the procedure in Article 6.
Those products which have not previously been marketed on the territory of the EU
fall outside the scope of the Regulation. They will have to comply with the technical
rules applicable in the Member State where they are put on the market for the first
time in the EU.

## Slide 47: Mutual recognition – part 4
The (intended) administrative decision must concern a product which is not subject to harmonised EU law
The Regulation operates in the non-harmonised area, in relation to products for which there is either no harmonisation of laws at EU level, or for aspects not covered by partial harmonisation (in the field of construction products see point 3 above).
The (intended) administrative decision must be addressed to an economic operator
Under Article 2(1), the Regulation applies to administrative decisions addressed to economic operators, whether taken or intended, on the basis of a ‘technical rule’, in respect of construction products lawfully marketed in another Member State, where the direct or indirect effect of that decision is the prohibition, modification, additional testing or withdrawal.
Any restrictive decisions taken by a national authority and addressed to any natural or legal person who is not an economic operator do not fall within the scope of the Regulation. An economic operator, as established by Article 2(18) of the CPR is, inessence, any person in the supply chain for the product concerned: its manufacturer, his authorised representative, its importer or distributor.
Thus - and without prejudice to Art. 36 TFEU – any restrictive decisions taken by competent authorities and addressed to any natural or legal person who is not an economic operator are not covered by the Mutual Recognition Regulation.

## Slide 48: Mutual recognition – part 5
The (intended) administrative decision must be based on a technical rule
The Mutual Recognition Regulation applies to (intended) administrative decisions taken on the basis of a ‘technical rule’ (Article 2(2)).
A technical rule is here defined as any provision of a law, regulation or other
administrative provision of a Member State:
(a) which prohibits the marketing of any products lawfully marketed in another
Member State in the territory of the Member State where the administrative
decision is or will be taken or compliance with which is compulsory when that
product is marketed in the territory of that Member State, and
(b) which lays down either:
• the characteristics required of that (type of) product, such as levels of quality,
performance or safety, or dimensions, including requirements as regards the
name under which it is sold, terminology, symbols, testing and test methods,
packaging, marking or labelling; or
• any other requirement which is imposed on that (type of) product for the
purposes of protecting consumers or the environment, and which affects its
life-cycle after it has been placed on the market, such as conditions of use,
recycling, reuse or disposal, where such conditions can significantly influence
the composition, nature or marketing of construction product.

## Slide 49: Mutual recognition – part 6
The direct or indirect effects of the (intended) administrative decision must be any of the following:
(a) prohibition of the placing on the market of that (type of) product;
(b) modification or additional testing of that (type of) product before it can be placed or kept on the market;
(c) withdrawal of that (type of) product from the market.
Any such (intended) decision must be taken in accordance with Article 2(1) of the Regulation.
Additionally, and in light of the Commission interpretative communication on the practical application of mutual recognition7, Member States are invited to insert into their draft national technical regulations mutual recognition clauses for products which have been lawfully manufactured and/or marketed in another Member State of the European Union or in Turkey, or lawfully manufactured in an EFTA State that is a contracting party to the EEA agreement.

## Slide 50: Mutual recognition – part 7
In the Czech Rep. this principle was implemented into the Act No. 22/1997 Coll., Article 13a
(1) A product manufactured in another Member State of the European Union or another state forming part of the European Economic Area shall be considered in individual cases as complying the requirements of this Order, providing it satisfies the tests and determinations carried out by a subject which was approved in the manufacturer’s state in accordance with methods valid in the Czech Republic or recognised as equivalent to them.
This article allows non-harmonized construction products legally placed on the market f.e. in Poland, Germany or Italy to be marketed in the Czech Republic without any further testing if their manufacturer or distributor proves they were properly tested in a country of origin.

## Slide 51: Market surveillance and safeguard procedures
Chapter VIII of the CPR
Role of Market Surveillance Authority (MSA) in the Czech Republic has been delegated to Czech Trade Inspection Agency (Česká obchodní inspekce). The Czech Trade Inspection Authority (CTIA) is an administrative government institution which falls under the jurisdiction of the Ministry of Industry and Trade of the Czech Republic. The Director General of the CTIA is appointed by the Minister of Industry and Trade. The CTIA was established under Act No. 64/1986 Coll., The Czech Trade Inspection Authority Act. The CTIA is a successor to the former State Trade Inspection. It consists of the Central Inspectorate and Regional Branch Inspectorates, whose headquarters are found in major regional cities.
Administrative Co-operation Group for the market surveillance for construction products (AdCo Construction) is composed of representatives of Member States' market surveillance authorities and was established to pursue the following objectives: the exchange of information between Member States' authorities concerning the national market surveillance mechanisms and the adopted solutions; the achievement of a uniformly high level of enforcement of the relevant EU legislation; to reduce the overlapping of national surveillance operations; to diffuse good market surveillance practices; to exchange views and solve practical problems. Documents are available at CIRCABC.

## Slide 52: Market surveillance and safeguard procedures
The biggest case - Fire doors with declared fire resistance
The inspection concerned construction products – doors with declared fire resistance. During tests, 3 out of 4 collected samples of doors did not comply with the declared parameters. Three tested types of wooden doors resisted the fire for only 5 to 7 minutes, instead of the 30 minute fire resistance declared by the manufacturer. Results of the subsequent laboratory assessment of the material composition confirmed in all three cases that these construction products did not comply with the approved type, i.e. samples tested within the certification of wooden door fire leaf, and they did not fulfill respective technical requirements. Due to the seriousness of the above mentioned findings, inspections of fire doors continued in cooperation with the Fire Rescue Service of the Czech Republic until the end of the year by collecting 4 more types of fire doors from 3 manufacturers and one foreign manufacturer. Also in this case, results of tests concerning the fire safety confirmed the previous findings, i.e. that fire doors distributed on the market in the Czech Republic did not fulfill requirements stipulated for fire safety. Only in 2015, all samples fulfilled the requirements.

## Slide 53: Market surveillance and safeguard procedures
Other cases
Thermal insulation systems, aperture fillings, combustion stationary sources with thermal input up to 500 kW (according to the Ministry of the Environment’s programme New Green Savings programme)
Construction materials in e-shops

## Slide 54: Using construction products in buildings
Czech Republic is not the best example of clear link between marketing construction products and using them in buildings. Regulatory competences are distributed among several ministries and their subordinated institutions.
Placing on the market is in competence of the Ministry of Industry and Trade and it´s subordinate offices like UNMZ and Czech Trade Inspection Agency. We are responsible for procedures described in the Acts no. 22/1997 Coll., 90/2016 Coll. and the CPR. On the other hand, construction products legally placed on the EU market in the Czech Republic have no guarantee they can be approved for using in buildings in our teritory. There is a strong competence of the Ministry of Regional Development and his subordinated regional building offices. Construction of roads and railways is in competence of the Ministry of Transport and its subordinate offices which issue their own directives, limiting the usage of construction products legally placed on the market.
A new act on construction products is been under preparation right now, with the aim to unify legislative in this field. It will take some time until it comes into full force though.

## Slide 55: EUROCODES
Eurocodes are a series of 10 European Standards, EN 1990 - EN 1999, providing a common approach for the design of buildings and other civil engineering works and construction products. They are the recommended means of giving a presumption of conformity with the basic requirements of the CPR for construction works and products that bear the CE Marking, as well as the preferred reference for technical specifications in public contracts.
The Eurocodes cover:
• basis of structural design (EN 1990);
• actions on structures (EN 1991);
• the design of concrete (EN 1992), steel (EN 1993), composite steel and concrete (EN 1994), timber (EN 1995), masonry (EN 1996), and aluminium structures (EN 1999);
• geotechnical design (EN 1997);
• the design, assessment, and retrofitting of structures for earthquake resistance (EN 1998).

## Slide 56: EUROCODES
Eurocodes apply to structural design of buildings and other civil engineering works including:
• geotechnical aspects;
• structural fire design;
• situations including earthquakes, execution and temporary structures.
For the design of special construction works (e.g. nuclear installations, dams, etc) other provisions than those in the EN Eurocodes might be necessary.
The Eurocodes are replacing national standards that provide common technical rules for the design of buildings and other civil engineering works and construction products.
Special website on Eurocodes
http://eurocodes.jrc.ec.europa.eu/

## Slide 57: EUROCODES
Standardisation - the European Commission sent a standardisation request mandating standardisation work (technical mandate M/515) to the European Committee for Standardisation (CEN). It also financially supports specific standardisation work.
Allowing Eurocodes in public tenders - according to the Public Procurement Directives (2004/17/EC and 2004/18/EC), contracting authorities in the EU must allow the use of Eurocodes in the structural design aspects of tenders.
Further harmonisation – the Joint Research Centre is assessing remaining national parameters for potential harmonisation. The centre also monitors and supports the standardisation work of CEN and provides input in technical discussions in the EU and beyond.
State of implementation of the Eurocodes in the European Union:
a document issued by the Commission in 2015 stated that the Eurocodes are implemented in 24 EU Member States. The use of all Eurocodes Parts is obligatory in the Czech Republic. Other EU members use selected parts of Eurocodes.

## Slide 58: selected Czech legislation relating to CONSTRUCTION PRODUCTs
-link-
Czech regulation aimed to fire safety
Czech regulation aimed to dangerous substances
Czech regulation aimed to radioactivity
Czech regulation aimed to water policy
Czech regulation aimed to biocidal products
Czech regulation aimed to construction and demolition wastes
Czech regulation aimed to ambient air protection
Czech regulation aimed to construction products coming into direct contact with water and intended for human consumption Czech regulation aimed to release of dangerous substances from construction products into indoor air
Czech regulation aimed to environmental impact assessment
Czech regulation aimed to noise emission
Czech regulation aimed to on energy management

## Slide 59: BASIC REQUIREMENT NO. 7 FOR CONSTRUCTION WORKS
Sustainable use of natural resources
The construction works must be designed, built and demolished in such a way that the use of natural resources is sustainable and in particular ensure the following:
(a) reuse or recyclability of the construction works, their materials and parts after demolition;
(b) durability of the construction works;
(c) use of environmentally compatible raw and secondary materials in the construction works.
Environmental Product Declaration (EPD) is a document that informs about the product’s environmental impact throughout its life cycle, from creation till its disposal. EPD provides measurable information about the material composition of the product, about the consumption of raw materials and energy in various stages of the product life cycle (product or service) and about the level of contribution (emission production) to the acidification of soil and water, water eutrophication, ozone depletion, the greenhouse effect and creating photochemical oxidants. The client receives objective information about the basic (technical) product characteristics, while also about the environmental performance of products, which allows the client to take into account the environmental aspects of the product while deciding which product to choose.
http://www.environdec.com

## Slide 60: EPD
EPD verification is a process where an independent organization (third party) verifies in place that the producer in accordance with the requirements of CSN EN ISO 14025 and other management documents processed EPD for his / their products.
EPD verification allows the producer to publish and present the EPD document. Producer thereby increases its value and prestige on the market and become a credible partner. Submission of independently verified EPD is conditional for cooperation with many institutions abroad, but also public authorities and local governments, for supply of works, goods or services. Our company has many years of experience, team of qualified experts and a number of satisfied customers.
Independently verified EPD is designed for all producers regardless of their focus and size who want to present the environmental performance of their of products (B2C).
Independently verified EPD is a useful tool for all producers who want to reduce the environmental impacts of their production, to optimize their manufacturing processes and products, and to present the environmental aspects of the product to the customers. Through independently verified EPD producers increase their competitiveness and get new market opportunities

## Slide 61: THANK YOU FOR YOUR ATTENTION.
Václava Holušová