## Slide 1: IPF5: Sub-Project WB17-MNE-TRA-03
Technical assistance for the preparation of
Preliminary Design and Environmental and Social Impact Assessment (ESIA)
for the bypass Podgorica (Smokovac-Tolosi-Farmaci)
of Bar-Boljare highway (SEETO Road Route 4)
Scoping report

## Slide 2: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Object:
  Bar-Boljare Motorway, Podgorica bypass (Farmaci-Tolosi-Smokovac) Approx. 16.5km
Services:
  Preliminary Design
  Environmental & Social Impact Assessment
  Securing building permits

## Slide 3: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Legislation
National Environmental Legal Framework regarding EIA, Resettlement issues etc.
EBRD Environmental and Social Policy 2014 (PRs 1-6, 8 and 10 applicable)
Category A, as per:
Art.6: Construction of motorways, express roads and lines for long-distance railway traffic; airports with a basic runway length of 2,100 meters or more; new roads of four or more lanes, or realignment and/or widening of existing roads to provide four or more lanes, where such new roads, or realigned and/or widened sections of road would be 10 km or more in a continuous length.

## Slide 4: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Project characteristics
Ref. No. | Characteristics | 
1 | Length (km) | 16.50
2 | Design speed (Ve- km/h ) | 120
3 | Minimal radius ( Rmin- meters) | 700
4 | The most unfavourable longitudinal gradient and length | 3.73%/306m
5 | Longitudinal gradient >4% (in percentages of total length) | 0%
6 | Third lane length | 0
7 | Maximum Embankment Height (m) | 25
8 | Maximum Cut Height (m) | 40
9 | Earthworks: | 
 | Embankments (m3) | 3,205,505.66
 | Cuts (m3) | 2,009,924.86
 | Balance between Cuts and Fills (m3) | 1,195,580.08
10 | Length of two way or twin bridges (m) | 2,729
11 | Length of twin tunnels (m) | 1,958
12 | Length of C&C (m) | 0
3 Interchanges (Farmaci, Zelenika, Tolosi) and 1 Interchange (Smokovac – out of the scope of this study, mentioned for the completeness of the study)
10 bridges
5 underpasses and 4 overpasses
2 twin tunnels
Box and circular highway culverts
One rest area, one motel and two petrol stations
Toll collection facilities

## Slide 5: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Typical cross section
Parameter | Value (120km/h)
Lane width | 4x3.75m
Emergency lane width | 2x2.50m
Edge strip width along the lanes | 2x0.50m
Edge strip width along the emergency lane | 2x0.25m
Median strip width | 4.00m

## Slide 6: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Earthworks balance
Earthworks | Quantity (m3)
Embankments (m3) | 3,205,506
Cuts (m3) | 2,009,925
Balance between Cuts and Fills (m3) | 1,195,581
Tunnel excavation material (m3) | 414,160
Net balance of earthworks | 779,421

## Slide 7: The Project
WB17-MNE-TRA-03: Podgorica Bypass
I/C Farmaci
Affected roads at the area of the interchange:
Existing road Podgorica – Centinje (NR, CH: 00+380.35). The road is maintained at the same location and it passes under the motorway with an underpass structure.
An existing vertical road, (VR, CH: 00+112.00). Road also passes under the motorway with an underpass structure. It is slightly shifted from its original location to achieve the required clearance in the underpass.
An existing side road (SR1). The road is affected by interchange’s branch 1 and it is relocated accordingly to preserve access to near-by properties.

## Slide 8: The Project
WB17-MNE-TRA-03: Podgorica Bypass
I/C Zelenika
Affected roads at the area of the interchange:
An existing access road, (Motorway’s CH: 04+770.00)
The new road passes under the motorway with an underpass structure. It is slightly shifted from its original location to achieve the required clearance in the underpass.
An existing access road, (Br1’s CH: 01+133.00)
The new road passes over branches 1 and 5 with an overpass structure. It is slightly shifted from its original location to achieve the required clearance in the underpass
.

## Slide 9: The Project
WB17-MNE-TRA-03: Podgorica Bypass
I/C Tološi
The bridges designed to support the development of the Tolosi Interchange are the 128m long Bridge T4 (Branch TBR4-1) at CH 0+150 and the 184m long Bridge T5 (Branch TBR1) at CH 0+040. In the area of Tolosi Interchange, reinforced embankments are used. The hydraulic design has indicated the need for the construction of 8 culverts in the Tolosi Interchange area (ramp sections),
.

## Slide 10: The Project
WB17-MNE-TRA-03: Podgorica Bypass
Tunnels
Ref. No | Chainage |  | Code Name | Name | Total Length (m)
 | From | To |  |  | 
1a | 4+980 | 6+470 | TN1-L | Zelenika Tunnel - Left | 1,490
1b | 4+944 | 6+470 | TN1-R | Zelenika Tunnel - Right | 1,526
2a | 8+140 | 8+580 | TN2-L | Velje Brdo - Left | 440
2b | 8+160 | 8+650 | TN2-R | Velje Brdo - Right | 490
 |  |  |  | Total | 3,946

## Slide 11: General Design – Main Alignment and Proposed Variant
WB17-MNE-TRA-03: Podgorica Bypass
Variant 1 (proposed alignment)
Variant 2
Farmaci
Tolosi
Smokovac

## Slide 12: Activity 3: Environmental and Social Impact Assessment (ESIA) – Scoping report
WB17-MNE-TRA-03: Podgorica Bypass
Environmental baseline
10 landscape types (Urban landscape, Semiurban landscape, Agricultural landscape, Cultural heritage landscape- Ancient city of Duklja, River Moraca landscape with canyon coasts, Landscape of Sitnica, Mareza and Zeta rivers, Forests areas landscape, Landscapes of maquis and bare terrain, Linear infrastructure landscape and Landscape of flooded areas (in the wider area)
Glaciofluvial (glf) and alluvial (al) Quaternary sediments, which are deposited over carbonate sediments of the Upper Cretaceous (K2), good to very good quality of rock mass
Terra rossa (red soil) is the main soil type – majority of the route as of medium erosion
Expected maximum of XIII degrees of MSC
One air and two noise monitoring stations from the national systems
Low flood risk, projection for increase of temperature and decrease of precipitation
Two rivers crossed (Zeta and Sitnica) and Moraca river in close distance, Mareza channel and others streams such as Shiralja (Rogami) crossed, available metric data for the stations for Zeta and Sitinica rivers, water quality data mainly for Zeta river
Majority of the area covered by rocks of low to very low permeability, several groundwater sources in the vicinity used for water purposed, most important water source of Mareza

## Slide 13: Activity 3: Environmental and Social Impact Assessment (ESIA) – Scoping report
WB17-MNE-TRA-03: Podgorica Bypass
Environmental baseline
Forests, grasslands, agricultural land, ruderal land, aquatic habitats
Seven 92/43 Annex I Habitat types (9250 Quercus trojana woods, 92A0 Salix alba and Populus alba galleries, 62A0 East sub-Mediterranean dry grasslands (Scorzoneretalia villosae), 6540 Sub-Mediterranean grasslands of the Molinio-Hordeion secalini, 6220* Mediterranean dry grasslands - Pseudo-steppe with grasses and annuals of the Thero-Brachypodietea, 3260 Water courses of plain to montane levels with the Ranunculion fluitantis and Callitricho-Batrachion vegetation and 3150 Natural eutrophic waterbodies with Magnopotamion and Hydrocharition)
4 plant species with special importance
Fauna: 3 gastropod species, 4 fish species, 1 amphibian, 4 bird species of special importance, the study on mammals is ongoing, but there is confirmed presence of bats
Nature park - Zeta River Volley (corresponds to IUCN category V of protected natural assets) with three protection zones, the project crosses for 1,25Km Zone III of sustainable use (zone with the least biodiversity importance)

## Slide 14: Activity 3: Environmental and Social Impact Assessment (ESIA) – Scoping report
WB17-MNE-TRA-03: Podgorica Bypass

## Slide 15: Activity 3: Environmental and Social Impact Assessment (ESIA) – Scoping report
WB17-MNE-TRA-03: Podgorica Bypass
Evaluation of alternatives
Ref. No | Criterion | Variant 1 |  | Variant 2 | 
1 | Excavations (m3) | 2,965,513 | 1.000 | 3,901,156 | 0.760
2 | Surplus of earthworks (m3) | 269,965 | 1.000 | 1,163,602 | 0.232
3 | Landscape (Visible length of bridges - m) | 2,729 | 0.896 | 2,446 | 1.000
4 | Noise (length of noise barriers - m) | 2,300 | 1.000 | 3,200 | 0.958
5 | Air & Noise Number of affected buildings | 1.37 | 1.000 | 82 | 0.841
6 | Number of Animal Passages / km of open route |  | 0.242 | 1.04 | 0.000
 | Total Environmental aspect scoring |  | 5.138 |  | 3.792
 | Average Environmental aspect scoring |  | 0.856 |  | 0.632
Ref. No | Criterion | Variant 1 |  | Variant 2 | 
1 | Length (km) | 16.5 | 1.000 | 17.38 | 0.949
2 | Physical & economical displacement (houses) | 21 | 0.952 | 20 | 1.000
3 | Impacts to arable agricurtural land (ha) | 39 | 1.000 | 42 | 0.929
4 | Impacts to curtural heritage (monuments) | 9 | Neutral | 9 | Neutral
 | Total Social aspect scoring |  | 2.952 |  | 2.878
 | Average Social aspect scoring |  | 0.984 |  | 0.959

## Slide 16: Activity 3: Environmental and Social Impact Assessment (ESIA) – Scoping report
WB17-MNE-TRA-03: Podgorica Bypass
Conclusions for scoping for impacts
All environmental parameters are scoped in, while waste and resources have negligible impacts.
Several surveys and modeling have been planned in order to achieve a better proposal for mitigation measures, i.e. air and noise modeling, 3D landscape images and targeted biodiversity surveys have been planned
Climate change resilience plan will be prepared
All social parameters were scoped. Even those with negligible impacts. The rationale behind is that some of the impacts might be exacerbated by the COVID-19 effects and impacts (such as GBV as part of a wider SEA/SH category), economic vulnerability might change significantly in the unfolding effects of the pandemic and alike.
The available secondary data are not readily available and have been supplemented by Social Assessments at local community and sampled household levels.

## Slide 17: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019
  1st and 2nd round of biodiversity surveys
  Air and noise measurements
  Air and noise modeling is being finalized
  3D landscape images are being prepared for determining the landscape and visual impacts
  Surface and groundwater measurements
  On site surveys and key informant interviews, focus group discussions etc. have been carried out for settlements affected by the Project
  The LARF (Land Acquisition and Resettlement Framework) is finalized

## Slide 18: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019
  1st and 2nd round of biodiversity surveys:
    1) flora and habitats, fish, amphibians and reptiles, birds – autumn 2019 and spring 2020
    2) mammals and bats – summer to winter 2020)
In order to define the habitats along the road alignment, several biodiversity surveys have been planned in a zone of 500m right and left from the alignment. Habitat and flora surveys were carried from September 2019 to June 2020, amphibians and reptiles survey was carried out in September 2019 and April – May 2020, birds surveys took place in September – October 2019 and late spring - early summer of 2020, fish survey in February 2020 while mammals and bats surveys are currently being carried out (July 2020 – December 2020).

## Slide 19: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019
  Air and noise measurements
  Air measurments have been carried out from 15.06-21.06.2020 at six points along or close to the proposed alignment, while the parameters measured were PM10, PM2.5, NO2, SO2 and CO.
  The results are being processed and will provide input as background air quality current situation for the air modelling that will calculate the emissions during the operation of the road.

## Slide 20: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  Air and noise measurements
  Noise measurments were measured at thirteen selected locations from 15th May to 13th June 2020 at points along or close to the proposed alignment. The parameters measured were Lday, Levening and Lnight. The results are being processed and will provide input as background air quality current situation for the air modelling that will calculate the emissions during the operation of the road.
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 21: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019
  Air and noise modeling is being finalized
The output of the noise modelling which will be in a table and map form and will be an appendix of the ESIA will indicate the necessity of additional noise mitigation measures.

## Slide 22: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  3D landscape images are being prepared for determining the landscape and visual impacts
will be prepared taking into account the structures that are proposed and the topography and landscape characteristics
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 23: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  Surface and groundwater measurements’ locations are being carried out
Sampling and analysis on four surface water locations:
Moraca river - Railway bridge (the location of Duklja) - 1340m southeast of the route of the highway
Zeta river - The location of Rogami bridge - 570m southeast of the route of the highway
Mareza river - The location of Mareza, south of the substation - 460m south of the route of the highway
Sitnica river - The location of Komanski bridge - 1400m south of the route of the highway
Sitnica River (Near Lekici)
Measured parameters: pH, Calcium, suspended solids, electrical conductivity dissolved oxygen, BOD5, COD, Nitrates, Nitrites, phosphates, ammonium, magnesium, total hardness, total alkalinity, chloride, sodium, potassium, carbonate, bicarbonate, total dissolved solids, mercury, aluminium, antimony, arsenic, cadmium, chrome, copper, lead, manganese, nickel, selenium, iron and zinc
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 24: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  Surface and groundwater measurements’ locations are being carried out
"Mareza" (Crack and cavernous porosity) - not affected by highway - 2300m north of the projected route of the highway
Well "Tološi„ - 220m south of the projected route of the highway
Well "Vineyard parcel of the Biotechnical Institute„ - 800m south of the projected route of the highway
"Farmaci" (Intergranular porosity) - 220m southeast of the projected route of the highway
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 25: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  Surface and groundwater measurements’ locations are being carried out
Testing parameters: physicochemical parameters of alkalinity, ammonia, calcium, chloride, colour, electrical conductivity, dissolved organic content, total hardness, magnesium, nitrate, nitrite, pH, potassium, sodium, sulphate, total dissolved solids, turbidity, iron, carbonate and bicarbonate and the microbiological parameters of E.Coli, total coliforms, fecal coliforms, streptococum, fecal streptococum, pseudomonas aeruginosa, legionella, clostridium and total count of microorganisms.
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 26: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  Surface and groundwater measurements’ locations are being carried out
The Water Directorate has been also asked to provide information for the position and characteristics of the water intake, quantity and quality of water, sanitary protection zones and water supply network (if they are in conflict with the route of the highway); Additionally, it has been asked to provide any relevant data for water supply design documents and sanitary Protection Zones design documents for sources:
• water supply for the settlement of Mrka
• water supply Zagoric for Podgorica
• water supply Okno for Piperi
• water supply Mareza for Podgorica
• water supply Farmaci for Ljesanska Nahija
• water supply Bolje sestre for the Regional Water Supply of the Montenegrin coastline
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 27: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  On site surveys and key informant interviews, focus group discussions etc. have been carried out for settlements affected by the Project
Identify the key environmental and socio-economic conditions in areas potentially affected by the Project and highlight those that may be vulnerable to aspects of the Project;
Describe their characteristics (nature, condition, quality, extent, etc.) now and in the future in the absence of the Project; and
Provide sufficient data to inform judgments about the importance, value and sensitivity/ vulnerability of resources and receptors to allow the prediction and evaluation of potential impacts.
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 28: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
  The LARF (Land Acquisition and Resettlement Framework) is finalized
  Meaningful and inclusive engagement, including empowered decision making in respect of eligibility for compensation and entitlements matrix, during preparation of LARF.
Activity 3: Environmental and Social Impact Assessment (ESIA)
Performed and planned activities/surveys since 2019

## Slide 29: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
Next phase
  Preparation of Environmental and Social Impact Assessment (ESIA), Stakeholder Engagement Plan (SEP), Resettlement Policy Framework (RPF), Non-Technical Summary (NTS),Environmental and Social Action Plan (ESAP) and assist beneficiary in Public consultation.
Key Issues
  Late selection and Approval of one of the presented variants in the draft Preliminary Design.
  Recently announced newly protected area (the already planned projects have been taken into consideration in the establishment of this area)
  COVID-19 related constraints related to travel and stakeholder engagement activities including political issues due to recent elections.
  IPF5 closing date (Submission of ESIA beyond that date)

## Slide 30: Description of Consultancy Services
WB17-MNE-TRA-03: Podgorica Bypass
THANK YOU